## Slide 1: SMART INDIA HACKATHON 2026
ZEIT
Two-Lane Adaptive Noise Cancellation for Defence Communications
Problem Statement ID — 26052
Problem Statement Title — AI/ML-enabled adaptive noise cancellation for stationary, non-stationary and impulsive defence noise
Theme — Miscellaneous
PS Category — Hardware
Organisation — DRDO · Department of Defence Production / IDEX
Team ID — HW2026106
Team Name — ZEIT v.1.0
Mentor — Dr. Swati Singal — Assistant Professor, CSE / SSCSE, Sharda University, Greater Noida

## Slide 2: ZEIT — Two-Lane Impulse-Adaptive Noise Cancellation
PROPOSED SOLUTION (DESCRIBE YOUR IDEA/SOLUTION/PROTOTYPE)
DETAILED EXPLANATION OF THE PROPOSED SOLUTION
LANE A · hearing protection · closes in under 1 ms · FxLMS on its own module
LANE B · transmit to radio · 25.3 ms end to end · eleven blocks on the Pi 5
Mic 3 · error
Mic 2 · reference
Mic 1 · voice
FxLMS filter
Anti-noise driver
The ear
Engine · 11 blocks
Vocoder · MELPe
Radio link
error signal — what still reaches the ear
HOW IT ADDRESSES THE PROBLEM
Impulsive noise — gunshots, artillery
Detect-and-react transient path, trained through the clipping with α-stable augmentation
Adaptive
A live kurtosis classifier retunes γ and β every frame — not tuned once, offline
High speech intelligibility
A dedicated voice guard, with DNSMOS SIG reported separately so over-suppression stays visible
Real-time on embedded hardware
23.7 K parameters at 39.6 MMAC/s — it runs on a Raspberry Pi 5, not a Jetson
INNOVATION AND UNIQUENESS OF THE SOLUTION
1
Two lanes, not one
Protection closes in under a millisecond; transmit tolerates 25 ms. Fusing them makes both impossible.
2
Detect, do not predict
Published deep ANC buys latency by predicting noise. A gunshot is unpredictable by definition.
3
RMS is undefined here
Heavy-tailed noise has infinite variance. We scale on percentile and fractional lower-order moments.
4
Measured, not downloaded
Calibrated gunshot data of our own, holdout split assigned before capture, checksum-frozen reference.
5
Crack before blast
0 · trigger
45.2 · crack
87.5 · blast
42.3 ms of warning
PROJECT HANDBOOK AND 3D WORKBENCH — LIVE DEPLOYMENT
https://zeit-handbook.netlify.app/
https://zeit-handbook.netlify.app/zeit-bench-3d

## Slide 3: TECHNICAL APPROACH
TECHNOLOGIES TO BE USED (E.G. PROGRAMMING LANGUAGES, FRAMEWORKS, HARDWARE)
C++17
real-time path
ONNX Runtime
inference on ARM
PyTorch
training, offline
GTCRN
23.7 K params
Aux-IVA
blind separation
BMRI
impulsive path
PFFFT
BSD FFT, not GPL
Raspberry Pi 5
8 GB, the engine
UMC202HD
2-ch capture
METHODOLOGY AND PROCESS FOR IMPLEMENTATION (FLOW CHARTS/IMAGES/ WORKING PROTOTYPE)
HARDWARE CHAIN — no development computer in the signal path
3 microphones
voice · reference · error
UMC202HD
24-bit, 48 V
Raspberry Pi 5
blocks 1–11
Communication unit
MELPe 2400 bps
Earcups
return audio
LANE B SIGNAL CHAIN — one 20 ms frame, 10 ms hop, 25.3 ms end to end
01
Audio in
02
Aux-IVA
03
Normalise
04
STFT + ERB
05 Classifier
kurtosis → γ, β
the adaptive decision — the system retunes per frame rather than being tuned once, offline
impulsive frame
stationary / non-stationary
06
BMRI — detect and interpolate
07
GTCRN — learned mask
recombine
08
Deep filter
09
Voice guard
10
Residual
11
ISTFT
→
Radio
LANE A CONTROL LOOP — SEPARATE MODULE, CLOSES IN UNDER 1 ms
Mic 2
reference
FxLMS W(z)
filtered-x
Driver → ear
anti-noise
Mic 3
in-ear error
error — the residual
OFFLINE PIPELINE — none of this ships; it shapes the weights that do
Range capture
96 kHz · calibrated
Measure
16 quantities
Validate
against holdout
Mix + augment
α-stable, clipped
Train
SI-SNR + L1
Prune + quantise
structured, INT8
Export ONNX
the only boundary
C++ engine
parity-tested
mismatch → retune the generator
25.3 ms algorithmic · 10 ms compute per hop · under 1 ms Lane A · 39.6 MMAC/s
SOURCE CODE — EVERY FIGURE IN THIS DECK IS REPRODUCIBLE FROM IT
https://github.com/Sarthakk1407/Zeit_at_SIH.git

## Slide 4: FEASIBILITY AND VIABILITY
ANALYSIS OF THE FEASIBILITY OF THE IDEA
23.7 K
parameters in the neural core
GTCRN · ICASSP 2024
25.3 ms
Lane B, end to end
20 ms frame · 10 ms hop
< 1 ms
Lane A loop, closed
anti-noise beats the wavefront
~₹12 k
prototype bill of materials
Pi 5 · UMC202HD · cooler · PSU
VERIFICATION CHAIN — EVERY NUMBER IN THIS DECK TRACES BACK TO A CHECKSUMMED ARTEFACT
Capture
96 kHz · 24-bit
GO / NO-GO
after every 3 shots
Calibrate
absolute dB SPL
Measure
54 quantities / shot
Freeze
SHA-256 data + engine
Compare
against the holdout
Reproduce
by config hash
reject → re-shoot, on site
PROOF OF EXECUTION — LIVE-RANGE GUNSHOT CAPTURE (OUR OWN DATA)
PRIMARY DATA · NOT A PUBLIC DATASET
Indoor range · staggered-gain two-channel rig · captured live on the ZEIT toolkit laptop
WHY THE RECORDING IS USABLE, NOT JUST DRAMATIC
2-channel staggered gain 18–24 dB apart — the cold channel survives the clip
96 kHz · 24-bit uncompressed WAV · limiter and high-pass OFF
Calibrated to absolute dB SPL with a reference tone, not relative dBFS
54 quantities measured per shot · 16 categories · frozen signature
Holdout split assigned before the first shot · SHA-256 freezes data + engine
GO / NO-GO validation after every three shots — a range is not repeatable
POTENTIAL CHALLENGES AND RISKS
STRATEGIES FOR OVERCOMING THESE CHALLENGES
One-shot range access — nothing is repeatable
GO / NO-GO after every three shots catches a bad take on site
The microphone clips on the blast, irreversibly
Staggered-gain pair 18–24 dB apart; the cold channel always survives
The Pi 5 throttles and latency drifts
Official cooler and 27 W supply are mandatory parts, not accessories
Targets move with input SNR
Reported as curves against input SNR, with the crossing point stated
A denoiser can be judged in the wrong place
The MELPe vocoder sits inside the evaluation chain — measured twice

## Slide 5: IMPACT AND BENEFITS
POTENTIAL IMPACT ON THE TARGET AUDIENCE
THE SOLDIER
140 dB
MIL-STD-1474 ceiling at the ear
Hearing protected — Lane A cancels at the eardrum in under 1 ms, before any processing happens.
Voice still gets out — commands survive the gunfire that used to bury them.
Situational awareness kept — listening mode preserves ambient sound; combat mode protects the voice.
THE UNIT AND ITS COMMANDER
~200 ms
of speech a single shot destroys
Fewer repeats — a command lands on the first transmission instead of the third.
Measured, not asserted — words lost per shot is a number, reported per weapon and per distance.
Works on the issued radio — MELPe 2400 bps, no new waveform to certify.
INDIAN DEFENCE INDUSTRY
₹12 k
prototype bill of materials
Indigenous IP — permissive licences end to end, no GPL, no foreign cloud.
Microcontroller-class — 23.7 K parameters runs on a Pi 5, not a Jetson.
Feeds a DRDO SDR — designed to drop into the software-defined radio programme.
WHAT ONE GUNSHOT COSTS, AND WHAT THE SYSTEM CHANGES
WITHOUT
Blast at 150 dB
arrives at the ear
~200 ms of speech lost
the impulse window
Command missed
words lost per shot
Repeat under fire
delay, and risk
WITH ZEIT
Lane A cancels at the ear
closed in under 1 ms
Lane B conceals, recovers
IRT target under 35 ms
Command lands
on the first transmission
Hearing preserved
MIL-STD-1474 respected
BENEFITS OF THE SOLUTION (SOCIAL, ECONOMIC, ENVIRONMENTAL, ETC.)
Health and social
Impulse noise is the leading cause of service-related hearing loss. Lane A protects the ear before any processing.
Operational
Voice survives the noise class the PS names first, and the system re-tunes per frame rather than being tuned once.
Economic
A microcontroller-class model instead of a Jetson: lower unit cost, lower power, longer field endurance.
Strategic
Indigenous IP and permissive licences — deployable under Make in India procurement, with no cloud dependency.
THE ENVELOPE THE SYSTEM WORKS INSIDE
> 15 dB
SNR
> 0.85
STOI
> 2.5
PESQ
< 25.3 ms
lane B
< 1 ms
lane A
< 6 W
board power
MATURITY PATH · bench integrated → range, calibrated data → field trial with a unit → radio integration → production, Make in India

## Slide 6: RESEARCH AND REFERENCES
DETAILS / LINKS OF THE REFERENCE AND RESEARCH WORK
HOW THE READING WAS USED
16
papers read end to end
11
inform the design — method, baseline, evidence
5
put code on the device
Widrow · Shao & Nikias · BMRI · GTCRN · H-GTCRN — one block each, named on slide 3.
WHERE THE PUBLISHED WORK STOPS
No impulsive noise in deep ANC.
Every result table uses engine, factory, babble and speech-shaped noise — not the class DRDO names first.
Latency is bought by prediction.
1.5–1.7 dB lost per 10 ms on periodic noise. A gunshot gives prediction nothing to work with.
RMS normalisation is invalid.
Heavy-tailed noise has infinite variance. The closest prior system normalises by RMS anyway.
Mic-side clipping is modelled by nobody.
Loudspeaker saturation is modelled carefully; a 140 dB blast destroys the waveform at the capsule.
THE SIXTEEN SOURCES
Foundations
Widrow — Adaptive Noise Cancelling, Proc. IEEE, 1975
Varga & Steeneken — NOISEX-92, 1993 · Shao & Nikias — FLOM, 1993
Learned enhancement
GTCRN — Rong, ICASSP 2024 · H-GTCRN, dual channel
DCCRN · FullSubNet · DeepFilterNet2 — real time on a Pi 4, 2022
Impulsive noise
Ruhland — BMRI, IEEE/ACM TASLP 23(10), 2015 · Ono — Aux-IVA, 2011
Yuan, Li & Kuruoğlu — α-stable noise, 2023 · Berger — IS³, 2025
Baselines, metrics and standards
Zhang & Wang — Deep ANC, 2021 · Tan — dual-mic DC-CRN, 2021
Le Roux — SDR, 2019 · Reddy — DNSMOS, 2022 · MIL-STD-1474 · JSS 55555
WHAT ACCOMPANIES THIS SUBMISSION
System Handbook
Ten figures, every block specified, every unverified figure marked as such.
zeit-handbook.netlify.app
3-D Prototype Workbench
Both lanes modelled, earcup cut away, a simulated shot traced end to end.
zeit-handbook.netlify.app/zeit-bench-3d
Architecture Audit
Thirteen ranked findings against our own design, each traced to a source.
in the repository
Source and data toolkit
21 CLI tools, the measurement engine, and the SHA-256 freeze.
github.com/Sarthakk1407/Zeit_at_SIH
EVERY FIGURE IN THIS DECK IS REPRODUCIBLE — the deck itself is built by script from the template, and the 3-D renders on slides 2 and 3 come out of the same model the handbook publishes.
Sixteen sources were read end to end and a gap analysis written against each. Five of them ship as code; the rest set the baseline we measure against, or the standard we are held to. Where our own review found a defect in this project's design, it is recorded in the audit rather than omitted — thirteen findings, ranked, with the four most serious answered on this slide.